Response time analysis:

Description:

The platform developed during this project may be used to develop a real-time application. In order to validate the platform a fictive application will be described, analysed and then used to validate the platform (time permitting).

The platform works with sporadic and periodic threads, as well as timers and mutexes (critical regions). It furthermore work with pre-emptive fixed priority scheduling and priority inheritance via the immediate ceiling priority protocol. These subjects have been discussed elsewhere in the report and will not be further elaborated here.

Experimental test application:

The experimental test application takes its basis in the set-up from Burns & Wellings figure 1.1, page 4. The set-up is elaborated with a sporadic task in the form of an on/off-button. This is shown in figure nn.

The first challenge is the shared data between the input flow reading and the output value angle, which are both periodic processes. The second challenge is the sporadic process monitoring the button, and its control of the other processes (stopping them). If we consider it an emergency-stop then the sporadic process must be able to pre-empt the other processes and stop them.

As it is possible for the input button process to simply “stop” the other processes there is technically no conflict between this process and the others, yet in order to make the example work a second set of shared data involving multiple primitives is introduced, which is set by the input button process and must be read by the other processes.

This, all in all, calls for two mutexes to protect the data shared between the input flow process and output valve process and the input button process and the other processes respectively.

Priority-wise we define the valve to always function on the newest data, thereby making the input flow reading the most important. The periods is simply chosen as is the deadlines (highest priority = highest number).

Process	Priority	Type	Period/ / min. interval	Deadline	Execution time / (no blocking)
Input button reading process	3	Sporadic	50ms	30ms	20ms
Input flow reading process	2	Periodic	500ms	200ms	35ms
Output valve angle process	1	Periodic	500ms	200ms	70ms

Furthermore we need to know the release jitter. This is defined by the scheduler, which in this platform is defined by the operating system; TS-Linux. Based on the specifications this may be determined to be 10us. Ignore release jitter, as it is negligible (and difficult to calculate)

We also need to determine the worst case execution time of the three processes. As there are potential blocking involved we have to factor this in, but for now we focus on the raw machine instruction execution time. By analysing the machine code for the three process we can set up the following colour-coded diagram for the execution.

If we define the exact execution time without blocking to

Process	Execution time
Input button reading process	20ms
Input flow reading process	35ms
Output valve angle process	70ms

Based on this we can perform the response time analysis and determine if the system will always meet its deadlines.

First we can do a graphical representation of the worst case, which is all processes being released simultaneous and the sporadic process continuously arriving at its minimum inter-arrival time. As the sporadic process is a stop-button it is naturally not feasible that it will arrive in this manor, and even if it did it would terminate the other processes, yet this fact will be ignored for this analysis.

Process	Execution time
Input button reading process	20ms
Input flow reading process	80ms
Output valve angle process	300ms

Unfortunately this is not necessarily the real worst-case (at least it might not be), as there is potential blocking from the lower-priority processes, as may be seen below.

Blocking causes priority inversion, causing the lower priority processes to be blocked by the higher priority processes. As we can see this causes the highest priority process to be delayed until almost 40ms, and if we placed the process initiations worst case (for the running-lock) we can delay it to a little over 40ms. The middle priority process also suffer blocking in this example. It is also possible to delay the low-priority process by simply changing the scheduling time.

So, how do we make sure we take all these possible scheduling-times into consideration? There are potentially an infinite amount of potential scheduling paths. Luckily there are mathematical formulas to help us with this.

Change to equations: Ri = Ci + Ii + Bi

Ri is the response time for process i.
Ii is the inteferrence imposed by higher priority processes on process i.
Bi is the blocking from lower priority processes suffered by process i.

Ii = sumj(ceiling(Ri/Tj)*Cj)

Bi = max(usage(K,i)*C(K))

The blocking is for ICCP only, other protocols have different blocking calculations. The Blocking equations can be simplified verbally to: “The cost of the single largest critical region in a lower priority process, which is also shared by process i”.

To manually calculate Ii requires a little more mathematics. This is due to the fact that Ri appear on both sides of the equation.

<insert equation>